## Slide 1: Frequency analyzer
Cst 120
By: An c. and drew d.

## Slide 2: Overview
Our project is a frequency analyzer
The input is sound, the output is the most dominant frequency

## Slide 3: Build materials
128x32 OLED Screen Arduino ID: 931
Electret Microphone Amplifier -MAX4466 with Adjustable Gain[ID: 1063]
Microchip ATmega328P
Custom made power regulator
16 MHz crystal oscillator
Furby

## Slide 4: SCHEMATIC for OLED

## Slide 5: OLED specs
Uses SSD 1306 driver chip to communicate with microcontroller via I2C
Screen contains 128 x 32 white OLED’s
We chose OLED because it does not require a back light, which decreases power consumption

## Slide 6: Schematic for power regulator

## Slide 7: Power regulator specs
LM7805 voltage regulator
2 x 0.1
1000V Silicone Diode

## Slide 8: Schematic for microphone

## Slide 9: Microphone module specs
Omnidirectional electret condenser microphone with operation frequency of 20-20,000 hertz
Includes a MAX 4465 op amp to amplify signal to the range 0-5 volts, centered at 2.5 for the Arduino

## Slide 10: Schematic for atmega 328p

## Slide 11: atmega 328p specs
28-pin AVR Microcontroller
I/O Pins: 23
Timers: Two 8-bit / One 16-bit

## Slide 12: Frequency determination
Drew to explain

## Slide 13: Software
Included Adafruit_GFX and Adafruit_SSD1306 libraries to interface with OLED
Utilized the FFFT library for fast Fourier transformation
Utilized Arduino 8.5 IDE
Microcontroller reads in the levels of audio signals coming from the microphone at a 6KHz sample rate
A fast Fourier transformation is applied determining coefficient of each frequency range
Outputs largest coefficient in hertz

## Slide 14: Possible improvements
Could add a dedicated ADC to get higher bit rate for more accurate conversion
Could add hardware high and low pass filters to remove unwanted noise

## Slide 15: DEMO

## Slide 16: Questions?